## Slide 1
WORKFLOW
INSTRUCTIONS
NOTES/OBSERVATIONS
TIME/DATE
☐ ≥ 50 ng/μL of total RNA per sample
or
☐ ≥ 500 ng/μL of total RNA per sample, if performing the Terminator treatment
(optional step) Add per sample:
☐ 1.3 μL of SuperScript III First-Strand Buffer (5x)
☐ 0.2 μL of Water
☐ 0.5 μL of Terminator Exonuclease (1 U/μL)
Mix by pipetting + spin down
Incubate at 30°C for 1 h
For each total RNA sample, add:
☐ 1 μL of a primers premix stock solution
☐ 1 μL of total RNA
Mix by pipetting 10 times carefully + spin down
Incubate at 65°C for 10 min
Transfer on ice for at least 2 min
Add per sample:
☐ 2 μL of SuperScript III First-Strand Buffer (5x)
☐ 1 μL of DTT (0.1 M)
☐ 2.5 μL of dNTPs (2.5 mM)
☐ 1.5 μL of Betaine (5 M)
☐ 1 μL of SuperScript III (200 U/μL)
Incubate at 22°C for 10 min, 50°C for 30 min, 75°C for 15 min, and hold at 4°C
☐ Add 18 μL of AMPure XP beads at RT
☐ Mix by pipetting 10x slowly and incubate for 5 min
☐ Pellet on magnet and pipette off the supernatant
☐ Keep on magnet, wash 3x with 200 μL fresh 70% EtOH, do not disturb the pellet
☐ Resuspend pellet in 30 μL water, incubate at RT for 5 min
☐ Pellet beads on magnet, elute purified first-strand cDNAs and transfer to new PCR tubes low-bind
Mix per qPCR replicate:
☐ 5 μL of Takara SYBR Premix Ex Taq (2x)
☐ 0.1 μL of cDNA PCR primer, Forward (10 μM)
☐ 0.1 μL of cDNA PCR primer, Reverse (10 μM)
☐ 0.2 μL of Rox Reference Dye II (50x)
☐ 3.1 μL of Water
☐ 1.5 μL of purified first-strand cDNA
☐ Analyze qPCR results
☐ Calculate the average Ct value for each cDNA sample
☐ Determine the optimum number (N) of
cDNA PCR cycles to be performed for each sample
☐ Pipettes 1000 μL, 200 μL, 10 μL, 2 μL
☐ Filtered Tips Low-bind
☐ 0.2 mL PCR tubes low-bind + caps
☐ 1.5 mL microcentrifuge tubes low-bind
☐ 96-well PCR plate low-bind
☐ 96-well Real-Time PCR plate
☐ Ultra-Pure Water
☐ Magnet for beads separation
☐ AMPure XP beads, resuspended and at room temperature
☐ Freshly prepared 70% EtOH, at room temperature
☐ Terminator Exonuclease (1 U/μL) / SuperScript III Reverse Transcriptase (200 U/μL) /
Takara SYBR Premix Ex Taq (2x), in freezer until needed
☐ SuperScript III First-Strand Buffer (5x) / DTT (0.1 M) / dNTPs (2.5 mM) / Betaine (5 M), on ice
☐ Trehalose/Sorbitol stock solution (3.3 M/0.66 M) / Reverse Transcription Random primers (100 μM) /
Template Switching Oligonucleotides (1 mM), on ice
☐ cDNA PCR primers Forward and Reverse (10 μM) / Rox Reference Dye II (50x), on ice
☐ RNA samples, in freezer until needed
Before start checklist:
nanoCAGE – DAY 1
RNA samples:
- Use a different barcode (primers premix solution) for each RNA sample and for each sample replicate
- Prepare the primers premix solutions in advance by mixing 1 μL of a Template Switching Oligonucleotide (1 mM) + 1 μL of Reverse Transcription Random primers (100 μM) + 8 μL of Trehalose/Sorbitol stock solution (3.3 M/0.66 M) – [store at -20°C]
- Trehalose/Sorbitol solutions are viscous; mix very carefully by pipetting up and down slowly for at least 10 times
- Prepare a master mix for the RT reaction
- Prepare a positive control of the RT reaction by using 1 μL of a control RNA sample
- Prepare a negative control of the RT reaction by using 1 μL of water
- Use in preference high quality total RNA to optimize nanoCAGE library preparation for best sequencing results
- Aspirate supernatant carefully
- In order to avoid losing the sample, be sure not to aspirate beads in the pipette tip together with the solution
- Analyze each first-strand cDNA and control samples in triplicates
- Prepare a master mix for the real-time qPCR reaction
- Prepare a negative control of the real-time qPCR reaction by adding 1.5 μL of water

## Slide 2
☐ Purified first-strand cDNA samples prepared on Day 1
Add for each sample:
☐ 25 μL of Kapa HiFi HotStart Ready Mix (2x)
☐ 0.5 μL of cDNA PCR primer, Forward (10 μM)
☐ 0.5 μL of cDNA PCR primer, Reverse (10 μM)
☐ 4 μL of Water
☐ 20 μL of first-strand cDNA sample
Mix by vortexing + spin down
Incubate at 95°C for 3 min, then perform [N] PCR cycles of 98°C for 15 s, 65°C for 10 s, 72°C for 2 min, and incubate at 72°C for 2 min, hold at 4°C
☐ Add 90 μL of AMPure XP beads at RT
☐ Mix by pipetting 10x slowly and incubate for 5 min
☐ Pellet on magnet and pipette off the supernatant
☐ Keep on magnet, wash 3x with 200 μL fresh 70% EtOH, do not disturb the pellet
☐ Resuspend pellet in 25 μL water, incubate at RT for 5 min
☐ Pellet beads on magnet, elute purified cDNA PCR products and transfer to new PCR tubes low-bind
☐ Use 3 μL of each purified cDNA PCR products samples for quantification by Quant-iT PicoGreen dsDNA assay
☐ Pool purified cDNA PCR products tagged with different barcodes together
[Mix at least 2 ng of each purified cDNA PCR products sample at this step]
☐ Use 3 μL of the pool of cDNA PCR products for quantification of the mix by Quant-iT PicoGreen dsDNA assay
(optional) ☐ Use 1 μL to visualize the size profile of the pool of cDNA PCR products and confirm the final concentration of the mix on an Agilent Bioanalyzer High Sensitivity DNA chip
☐ Pipettes 1000 μL, 200 μL, 10 μL, 2 μL
☐ Filtered Tips Low-bind
☐ 0.2 mL PCR tubes low-bind + caps
☐ 1.5 mL microcentrifuge tubes low-bind
☐ 96-well PCR plate low-bind
☐ 384-well microplate for fluorescence assays
☐ Ultra-Pure Water
☐ Kapa HiFi HotStart Ready Mix (2x), on ice
☐ cDNA PCR primers, Forward and Reverse (10 μM), on ice
☐ Magnet for beads separation
☐ AMPure XP beads, resuspended and at room temperature
☐ Freshly prepared 70% EtOH, at room temperature
☐ Lambda DNA standard stock solution (1 ng/μL), on ice
☐ Quant-iT Picrogreen Reagent (200x), in fridge until use
☐ TE buffer (1x), at room temperature
☐ Bioanalyzer DNA High Sensitivity DNA kit, at room temperature 30 min before use
☐ Purified first-strand cDNA samples, on ice
Before start checklist:
nanoCAGE – DAY 2
Purified First-Strand cDNA samples:
- Aspirate supernatant carefully
- In order to avoid losing the sample, be sure not to aspirate beads in the pipette tip together with the solution
WORKFLOW
INSTRUCTIONS
NOTES/OBSERVATIONS
TIME/DATE
- It is also possible to mix purified cDNA PCR products tagged with different barcodes by group/experimental condition and further perform one tagmentation reaction per group using one Nextera N-series Index primer per reaction, and then pool the different nanoCAGE libraries obtained together, prior to library quantification and sequencing
- The concentration of the mix should be at least 0.1 ng/μL and the volume of at least 2.5 μL in order to perform the tagmentation reaction
- Prepare 5 μL of a 1 ng/μL dilution of the pool of cDNA PCR products and measure the concentration of the dilution in triplicate by applying 3 × 1 μL on the Bioanalyzer chip
- Quantify the cDNA products in the 100 bp – 9,000 bp range
- Prepare a master mix of the cDNA PCR reaction, including extra volumes for the positive and negative controls of the RT reaction
- Perform [N] cDNA PCR cycles for each first-strand cDNA sample based on the Ct values obtained from the real-time qPCR experiment performed on Day 1

## Slide 3
WORKFLOW
INSTRUCTIONS
NOTES/OBSERVATIONS
TIME/DATE
☐ Quantified pool(s) of purified cDNA PCR products prepared on Day 2
☐ Prepare ≥ 2.5 μL of a dilution of the pool at
0.1 – 0.2 ng/μL
Add in PCR tube low-bind:
☐ 5 μL of Tagment DNA Buffer
☐ 2.5 μL of the dilution of the pool of cDNA PCR products (0.25 – 0.5 ng)
☐ 2.5 μL of Amplicon Tagment Mix
Incubate at 50°C for 10 min, Hold at 10°C
☐ Add 2.5 μL of NT buffer as soon as the temperature reaches 10°C
Mix by pipetting 10x carefully and incubate 5 min at RT
Add:
☐ 2.5 μL of a Nextera XT N-series Index primer
☐ 2.5 μL of nanoCAGE custom S-series primer (10 μM)
☐ 7.5 μL of Nextera PCR Mastermix
Mix by pipetting carefully, spin down briefly
Incubate at 72°C for 3 min, 95°C for 30 s, then perform 12 PCR cycles of 95°C for 10 s, 55°C for 30 s, 72°C for 1 min, and incubate at 72°C for 5 min, hold at 10°C
☐ Add 22.5 μL of AMPure XP beads at RT
☐ Mix by pipetting 10x slowly and incubate for 5 min
☐ Pellet on magnet and pipette off the supernatant
☐ Keep on magnet, wash 3x with 200 μL fresh 70% EtOH, do not disturb the pellet
☐ Resuspend pellet in 20 μL water, incubate at RT for 5 min
☐ Pellet beads on magnet, elute purified cDNA PCR products and transfer to a new PCR tube low-bind
☐ Prepare ≥ 20 μL of 1:10 and 1:20 dilutions of the purified nanoCAGE library
☐ Use 3 × 1 μL of purified nanoCAGE library and 3 × 1 μL of the 1:10 and 1:20 dilutions to visualize the size profile of the nanoCAGE library and confirm the final concentration on an Agilent Bioanalyzer High Sensitivity DNA chip
(optional) ☐ Use 3 μL of the dilutions 1:10 and 1:20 of the purified nanoCAGE library for quantification by Quant-iT PicoGreen dsDNA assay
☐ Prepare the nanoCAGE library for sequencing according to the protocol and recommendations provided by Illumina for the sequencing system selected
☐ Pipettes 1000 μL, 200 μL, 10 μL, 2 μL
☐ Filtered Tips Low-bind
☐ 0.2 mL PCR tubes low-bind + caps
☐ 1.5 mL microcentrifuge tubes low-bind
☐ 96-well PCR plate low-bind
☐ 384-well microplate for fluorescence assays
☐ Ultra-Pure Water
☐ Magnet for beads separation
☐ AMPure XP beads, resuspended and at room temperature
☐ Freshly prepared 70% EtOH, at room temperature
☐ Lambda DNA standard stock solution (1 ng/μL), on ice
☐ Quant-iT Picrogreen Reagent (200x), in fridge until use
☐ TE buffer (1x), at room temperature
☐ Bioanalyzer DNA High Sensitivity DNA kit, at room temperature 30 min before use
☐ Tagment DNA Buffer / NT Buffer, on ice
☐ Amplicon Tagment Mix / Nextera PCR Mastermix, in freezer until needed
☐ 12 Nextera N-series Index primers / nanoCAGE custom S-series primer (10 μM), on ice
☐ NaOH 5 M, pH ≥ 13/ Qiagen EB buffer, at room temperature
☐ Illumina sequencing kit (e.g., MiSeq Reagent Kit v2) / PhiX Sequencing Control v3 / nanoCAGE Sequencing primer Read 1 (100 μM), in freezer until needed
☐ Quantified pool(s) of purified cDNA PCR products, on ice
Before start checklist:
nanoCAGE – DAY 3
Quantified pool(s) of cDNA PCR products:
- Either one pool containing all cDNA PCR products samples or several pools containing cDNA PCR products samples grouped by experimental condition
- Mix NT buffer carefully in order to avoid the formation of bubbles
- If processing several pools of cDNA PCR products, choose one Nextera N-series Index primer per pool when performing the Reduced-Cycle PCR Amplification
- If processing a single pool of cDNA PCR products, perform the PCR reaction using a single Nextera N-series Index primer and do not sequence the index. Alternatively, perform the PCR using 2.5 μL of an equimolar mix of the 12 Nextera N-series Index primers (i.e., mix 2 μL of each primer) and sequence the index
- Aspirate supernatant carefully
- In order to avoid losing the sample, be sure not to aspirate beads in the pipette tip together with the solution
- If processing several nanoCAGE libraries prepared from different groups of samples, first quantify each library individually, then prepare a mix by adding equal quantities of each library and quantify dilutions of the pool as indicated
- Quantify the nanoCAGE library by selecting nanoCAGE fragments in the 150 bp – 1,500 bp range
- In general, sequence the nanoCAGE library at a concentration of 6 – 12 pM
- Add 10% of PhiX Sequencing Control library to the final nanoCAGE sequencing sample
- Output sequencing data as FASTQ files for bioinformatics analysis and demultiplexing based on barcode, index, and UMI informations